## Slide 1
Innovations in Munitions Response Investigations
Steve Saville Jacobs
Summer 2023

## Slide 2: Disclaimer
This seminar is intended to be informational and does not indicate endorsement of a particular product(s) or technology by the Department of Defense or NAVFAC EXWC, nor should the presentation be construed as reflecting the official policy or position of any of those agencies. Mention of specific product names, vendors, or source or information, trademarks, or manufacturers is for informational purposes only and does not constitute an endorsement or recommendation by the Department of Defense or NAVFAC EXWC. Although every attempt is made to provide reliable and accurate information, there is no warranty or representation as to the accuracy, adequacy, efficiency, or applicability of any product or technology discussed or mentioned during the seminar, including the suitability of any product or technology for a particular purpose.

## Slide 3: Presentation Overview
Introduction
Background on MR Technologies
SLAM overview
One-Pass AGC overview
Quality Requirements for MR projects
Conclusions and Useful References
AGC: Advanced Geophysical Classification
MR: munitions response
SLAM: simultaneous localization and mapping

## Slide 4: Speaker Introduction
Steve Saville
Geosyntec-Jacobs JV
BS (’99), MS (’07) Geology, PG (’07)
Past 6 years working Navy CLEAN MR
Started in UXO Geophysics in 2001… and never thought MMRP would last this long!
Originally from North Carolina, spent part of childhood across the Chesapeake from Annapolis and has lived in eight states from Hawai’i to Tennessee
Not Pictured: Cats (2), Martha and Mr. Coffee. They prefer it this way.
CLEAN: Comprehensive Long-term Environmental Action—Navy
MMRP: Military Munitions Response Program
PG: Professional Geologist
UXO: unexploded ordnance

## Slide 5: Speaker Introduction
Steve Saville
Fun Facts
  Canoed solo from Montana to New Orleans, 2,815 miles, 97 nights, zero smartphones
  Enjoys all most aspects of baseball… for example, early in the season, in 40°F, with a five-run lead late in the game to a non-conference team
(USGS 2023)
(SEC Network 2019)

## Slide 6: Presentation Overview
Introduction
Background on MR Technologies
SLAM overview
One-Pass AGC overview
Quality Requirements for MR projects
Conclusions and Useful References

## Slide 7: Background on MR Technologies
Background on MR Technologies
Problem statements
MEC is an acute and potentially lethal hazard
MEC may be present in subsurface for decades, requiring management or remediation of site
Geophysical tools can detect and classify subsurface metallic objects, but:
  Accurate positional data are needed (Part 1 of this presentation)
  Most subsurface metallic objects are not munitions-related (Part 2)
MEC: munitions and explosives of concern
Notes: MEC should be put in context with regards to munitions items in general. While MEC is the hazard, munitions items (MPPEH) in general can generate actions for DoD.

## Slide 8: MR Technologies and their Objectives
Positioning
Detection
Advanced Geophysical Classification
(USACE 2020)
Background on MR Technologies
(USACE 2021)

## Slide 9: MR Technologies and their Objectives
Positioning – we must be able to know where things are
  GPS
    DGPS – lower accuracy than MR requirements
    RTK – standard for MR geophysical surveys
  What about where GPS does not work
    Fiducial – lowest accuracy
    Robotic Total Station
      Accuracy on par with RTK
      Less efficient than RTK
    SLAM
DGPS: differential Global Positioning System
GPS: Global Positioning System
RTK: real-time kinematic
Background on MR Technologies
(Jacobs 2023)
Notes: RTS: dropouts and “shadows” occur behind trees and other obstructions

## Slide 10: MR Technologies and their Objectives
Detection – find the metal
  Magnetometers (but only ferrous metal)
  Electromagnetic induction sensors (all metals)
Background on MR Technologies
(Jacobs 2023)
(Jacobs 2023)
(Geomatrix 2023)
Notes: These are the first widely used digital tools for UXO detection, pre-dating the establishment of MMRP in 2001.
Magnetometers were the instruments of choice in the 1990s, then the EM61 (center) became heavily used beginning around 2000. Multi-axis AGC sensors were in development in the mid-2000s and were ready for contractor demonstrations circa 2010.

## Slide 11: MR Technologies and their Objectives
Classification – focus on the munitions
  As we covered, most subsurface metallic objects are not munitions related
Background on MR Technologies
(Jacobs 2023)

## Slide 12: MR Technologies and their Objectives
Classification – focus on the munitions
  AGC uses advanced sensors to collect a tremendous amount of data, then software to invert data to identify source(s) – that is, tangible objects – most likely to have caused the measured data
Background on MR Technologies
(Jacobs 2023)
(Jacobs 2023)
(Jacobs 2023)
Notes: Inversion = mathematical process to identify the cause(s) behind measured data

## Slide 13: AGC Data Collection in One Slide
What are advanced sensors? What is “multi-axis EM”?
EM: electromagnetic
mV/A: millivolt(s) per amp
ms: millisecond(s)
Background on MR Technologies
(NAVFAC EXWC 2023)
Notes: Dated video. For general illustration only. Subsurface sources can be illuminated from multiple axes (Z transmitter not solely responsible for deriving one/all polarizability). All received data are assembled/inverted to solve for source(s) location, depth, and polarizabilities. There are more time gates in AGC sensors than EM61 and response data are recorded in three dimensions (vice one with the EM61).

## Slide 14: AGC Data Analyses in One Slide
Same physics as DGM
Specifically designed for munitions classification
Interrogates subsurface object from all directions
Now we can isolate intrinsic features useful for classification (answer independent of location)
Polarizability Property | Target Property
Decay Rate | Wall Thickness
Relative Magnitude | Shape
Total Magnitude | Size (Volume)
DGM: digital geophysical mapping
Background on MR Technologies
(Jacobs 2023)
Notes: AGC is not viable at all sites. High densities of metal objects in the subsurface (e.g., trash pits) and high geologic response (e.g., highly conductive soil) reduce ability to resolve and correctly classify objects.
Decay=slope of curves. Steeper slope = thinner wall.
Relationship of curves = shape. 1=2=3: sphere. 1=2>3: disc. 1>2=3: cylinder.
Y-intercept, y-values = size.

## Slide 15: Background on MR Technologies
CSM: conceptual site model
Background on MR Technologies
Along with intrusive data, these technologies advance the CSM
(Jacobs 2023)
Notes: CSM is putting the investigation’s purpose and data into context of the risks to humans and the environmental.

## Slide 16: Background on MR Technologies
Along with intrusive data, these technologies advance the CSM (including the vertical CSM)
mm: millimeter(s)
Background on MR Technologies
LEGEND
Deepest recovered UXO
Amplitude response detection limit
(Jacobs 2023)
Notes: Though this CSM includes 75mm projectiles and 5-inch rockets, neither were recovered during Remedial Investigation. This may be the case at other/future sites. Point is that understanding depth of reliable detection and classification is important for all munitions types that may be at a site.

## Slide 17: Presentation Overview
Introduction
Background on MR Technologies
SLAM Overview
One-Pass AGC Overview
Quality Requirements for MR Projects
Conclusions and Useful References
Notes: With introduction to MR technologies complete, the next section will cover SLAM, a positioning technology (recall the top three concepts: Positioning, Detection, and Classification)

## Slide 18: What is SLAM?
Walk through and scan environment
3D map is generated in real time
Mapped data used to create a 3D model
Accurate colorization and texture
LiDAR: light detection and ranging
SLAM Overview
Simultaneous Localization and Mapping is a positioning technology
Scans with high precision LiDAR while in motion
Builds 3D model in real time and tracks position without GPS
Allows for high accuracy positional data in GPS-denied environments
(Jacobs 2023)
Notes: “LiDAR” covers a variety of forms and applications. LiDAR may be used to see through vegetation (i.e., the last return). In this application, LiDAR is using first, second, and strongest return information to develop 3D model.

## Slide 19: What is SLAM?
Simultaneous Localization and Mapping is a positioning technology
Scans with high precision LiDAR while in motion
Builds 3D model in real time and tracks position without GPS
Allows for high accuracy positional data in GPS-denied environments
For total coverage requirements in MRSs, GPS-compromised
is
GPS-denied!
MRS: munitions response site
SLAM Overview
(Jacobs 2023)
(USACE 2012)

## Slide 20: What is SLAM?
SLAM is a combination of hardware, software, and workflow to:
Develop a point cloud map
Establish the sensor’s location within it
Navigate through it
Output positional data in real time to a geophysical sensor
SLAM Overview
(Jacobs 2023)

## Slide 21: What is SLAM?
SLAM Overview
  Back to the concept…
  How does this actually work?

## Slide 22
SLAM Overview
(Kaarta 2021)
Notes: Context: consider this the room we are in. Bottom plane of cube is the ground surface, the room’s floor.

## Slide 23
SLAM Overview
(Kaarta 2021)

## Slide 24
IMU: inertial measurement unit
SLAM Overview
(Kaarta 2021)
Notes: IMU measures changes in acceleration on X,Y,Z axes, as well as angular velocity.

## Slide 25
SLAM Overview
(Kaarta 2021)

## Slide 26
SLAM Overview
(Kaarta 2021)

## Slide 27
SLAM Overview
(Kaarta 2021)

## Slide 28
Hz: hertz
SLAM Overview
(Kaarta 2021)

## Slide 29
SLAM Overview
(Kaarta 2021)

## Slide 30
SLAM Overview
(Kaarta 2021)

## Slide 31
SLAM Overview
(Kaarta 2021)

## Slide 32
SLAM Overview
(Kaarta 2021)

## Slide 33
SLAM Overview
(Kaarta 2021)

## Slide 34
SLAM Overview
(Kaarta 2021)
Notes: Accuracy is best when Roll, Pitch, and Yaw are less than 15 degrees. Consider using Camera Mode if using in steeper terrain.

## Slide 35
SLAM Overview
(Jacobs 2023)
Notes: A point cloud map is created of the GPS-denied environment, then the SLAM sensor localizes and navigates within it, outputting positional data in real time to geophysical sensors.

## Slide 36: What is SLAM?
  Now we can take AGC (and other technologies) into the woods at our MRSs.
SLAM Overview
(Jacobs 2023)

## Slide 37: Benefits of SLAM
  Now we can take AGC (and other technologies) into the woods at our MRSs.
This allows for more defensible data across an entire site and potential scope, schedule, and budget benefits:
  Accurate positional data allow for application of AGC
  AGC’s improved data quality adds assurance that investigative goals are met
  Allows for an even application of the investigation (compared to mixing AGC, fiducial DGM, and analog)
  Better RIs lead to better Remedial Designs/Remedial Actions and outcomes
  Generation of 3D model can be applied to the CSM (digital elevation model, and vertical distribution of MEC)
RI: Remedial Investigation
SLAM Overview
(Jacobs 2023)
Notes: Positional information may be good from year to year (trees grow slowly). Refer to Camp Blanding lessons learned (USACE/Heaton, NAOC 2022).
Reduces need for Professional Land Surveyors because SLAM can be used for reacquisition (i.e., returning to a selected geophysical anomaly or source for intrusive investigation).

## Slide 38: SLAM + AGC Case Study Results
2020 Pilot Study at Marine Corps Base Quantico
SLAM Overview
Dynamic MetalMapper 2x2 survey
  100-foot by 100-foot grids
  Data collection performed with concurrent RTK + SLAM positional data
    Blue: RTK-GPS positions
    Red/Green/Yellow: SLAM positions
  Typical RTK-to-SLAM difference: 0.07 meter
(Jacobs 2023)

## Slide 39: SLAM + AGC Case Study Results
2020 Pilot Study at Marine Corps Base Quantico
DAM: dynamic acquisition mode
GDB: geophysical database
m: meter(s)
MPC: Measurement Performance Criteria (Pass/Fail)
QC: quality control
Dynamic MetalMapper 2x2 survey
  100-foot by 100-foot grids
  Data collection performed with concurrent RTK + SLAM positional data
Dynamic detection and positioning accuracy assessed through QC seeds
  Center of circle: QC seeds’ coordinates
  Blue dots: targets’ coordinates
SLAM Overview
(Jacobs 2023)

## Slide 40: SLAM Interactive: Break for questions and comments

## Slide 41: Presentation Overview
Introduction
Background on MR Technologies
SLAM Overview
One-Pass AGC Overview
Quality Requirements for MR Projects
Conclusions and Useful References

## Slide 42: Basics of AGC Workflow
Detect-then-Cue Classification (‘Traditional’ AGC)
  An area is mapped dynamically to detect and target subsurface sources that may be MEC
    These targets are then visited with an AGC sensor to collect cued AGC data
      The cued AGC data are processed, and TOI/Non-TOI are classified
        TOI are intrusively investigated
One-Pass Classification
  An area is mapped dynamically to detect and target subsurface sources that may be MEC
    The dynamic AGC data are processed, and TOI/Non-TOI are classified
      TOI are intrusively investigated
One-Pass AGC Overview
TOI: target of interest
  Q: Why would anyone detect then cue?
  A: Because we had no other option!*
* opinion of presenter
Notes: Note: Industry use of AGC developed largely through demonstrations in which accepted DGM methods (e.g., full coverage EM61 data+maps) were supplemented by cued AGC data collection and analyses. Initially, more data (and stationary data) collected over an unknown subsurface source were needed for reliable classification of the source(s).
Regulatory acceptance of, or familiarity with, cued AGC was supported via Interstate Technology and Regulatory Council documents and training. Department of Defense Advanced Geophysical Classification Accreditation Program has since recommended and ‘regulated’ the use of AGC.

## Slide 43: Cued AGC versus One-Pass AGC
Similarities:
Both provide a richer data set allowing for better guidance for intrusive investigation and follow-on remedial action alternatives
Both ultimately result in classification of sources
Both reduce number of digs required by approximately same amount
Both have similar limits on classification in high-density situations
Both have several DAGCAP-validated sensors to choose from in varying form factors
One-Pass AGC Overview
DAGCAP: DoD Advanced Geophysical Classification Program
(Jacobs 2023)

## Slide 44: Cued AGC versus One-Pass AGC
Differences:
Detect-then-cue requires two phases of fieldwork
  Two field surveys, two rounds of processing, two rounds of QC, an extra step to report
One-Pass AGC is completed in a single phase of fieldwork
  Single field survey, one round of processing, one round of QC, fewer steps to report
  Background leveling problems obviated
  Fewer steps for nonconformances
Industry has more experience with detect-then-cue, but is rapidly gaining experience with one-pass
One-Pass AGC Overview
(Jacobs 2023)

## Slide 45: Workflow: Cued versus One-Pass
Intrusive Investigation
of TOI
Verification/Validation Digs
Final DUA
Cued Survey
Initial Prioritized List
Training Digs
Prioritized Dig List
Site-specific Library Finalized
Cued AGC DUA
Initial Planning/Initial TOI Library
Detection Survey/Target Selection
Initial DUA
Intrusive Investigation
of TOI
Verification/Validation Digs
Final DUA
Initial Planning/Initial TOI Library
One-Pass AGC Survey
Training Digs
Site-specific Library Finalized
Prioritized Dig List
One-Pass DUA
Cued Workflow
One-Pass Workflow
DUA: data usability assessment
One-Pass AGC Overview
Notes: Note: Many MR- and AGC-specific terms used.
Focus on the blue boxes – fewer steps. And the “Cued Survey” step may appear small in a flowchart, but as illustrated on Slide 51, can involve thousands of cued measurements and weeks of data collection and processing.

## Slide 46: Workflow: Cued versus One-Pass
Intrusive Investigation
of TOI
Verification/Validation Digs
Final DUA
Cued Survey
Initial Prioritized List
Training Digs
Prioritized Dig List
Site-specific Library Finalized
Cued AGC DUA
Initial Planning/Initial TOI Library
Detection Survey/Target Selection
Initial DUA
Intrusive Investigation
of TOI
Verification/Validation Digs
Final DUA
Initial Planning/Initial TOI Library
One-Pass AGC Survey
Training Digs
Site-specific Library Finalized
Prioritized Dig List
One-Pass DUA
Cued Workflow
One-Pass Workflow
One-Pass AGC Overview
Notes: Note: Many MR- and AGC-specific terms used.
Focus on the blue boxes – fewer steps. And the “Cued Survey” step may appear small in a flowchart, but as illustrated on Slide 51, can involve thousands of cued measurements and weeks of data collection and processing.

## Slide 47: AGC Sensors Commercially Available
Detect-then-Cue AGC Sensors
TEMSENSE: used at MCB Quantico
  Firm vendor requirements for its use; very specific training
  Vendor is knowledgeable and generally responsive/supportive
  Currently only a single unit available for rent
  Good in similar environments to EM61
MetalMapper 2x2: used on many Navy and Army sites
  Known to have “issues,” difficulties on some sites
  Limited technical support at times
  Only a few units available for rent
  Good in similar environments to EM61
MPV: smaller, agile, person-portable
  Several for rent, have been in demand
  Good for sites with limited accessibility
TEMSENSE
MPV
MM 2x2
MPV: Man Portable Vector
One-Pass AGC Overview
(Jacobs 2023)
(TEMSense 2023)
(ESTCP)
Notes: AGC sensor malfunctions and responsiveness of technical support need to be understood as potential factors to project schedules.
MetalMapper 2x2 “issues”: drift and background correction, the latter not due to MetalMapper itself, but rather the cued AGC approach.

## Slide 48: AGC Sensors Commercially Available
One-Pass AGC Sensors
TEMSENSE
  Same sensor as for detect-then-cue
  Contractors and Government can process data using Geosoft
APEX: has been used at Naval Air Station Oceana
  Many units available for rent
  Many units have been sold into industry (i.e., >20)
  Good in similar environments to EM61
UltraTEM: has been used at Army installations
  Vendor also performs processing; a Geosoft option is “coming soon”
  Multiple form factors – Towed Array to person-portable
  Demonstrated success at large sites
  Person-portable validated, more agile form factors on the way
APEX
UltraTEM
One-Pass AGC Overview
(Jacobs 2023)
(Weston 2023)

## Slide 49: AGC Project Spotlight – Remedial Investigation at Dam Neck Annex
Moving Target Mortar Range – North
2010 SI → 2018 ESI → 2020 RI start → 2022 RI field start
Approximately 5 acres of RI
Tight schedule to minimize disruptions to classroom building
AGC used for better data and to focus intrusive investigation
GPS-denied areas, so SLAM used for positional data
ESI: Expanded Site Inspection
SI: Site Inspection
One-Pass AGC Overview
(Jacobs 2023)

## Slide 50
One-Pass AGC Overview
Moving Target Mortar Range – North
2020 plan was to perform detect-then-cue
MetalMapper 2x2 undermined by sensor issues (noise leading to QC fails, unusable data)
Team regrouped, selected one-pass AGC for best outcome and for classifying previous DGM targets that were to be cued with AGC
Intrusive successfully completed with minimal disruption to classroom building users
AGC Project Spotlight – Remedial Investigation at Dam Neck Annex
(Jacobs 2023)

## Slide 51: AGC Project Spotlight – Remedial Investigation at Dam Neck Annex
One-Pass AGC Overview
Moving Target Mortar Range – North
Initial dynamic MetalMapper 2x2 data (where thought to be usable) indicates ~1,000 sources per acre would need cued AGC
Interim one-pass AGC results showing similar sources per acre, with good reductions without need for cued AGC
APEX one-pass AGC data over same area – good agreement between data sets
MetalMapper 2x2 AGC data
APEX data. Squares are detections, Xs are required digs.
(Jacobs 2023)

## Slide 52: AGC Project Spotlight – Remedial Investigation at Dam Neck Annex
One-Pass AGC Overview
Had 1,000 sources per acre that needed cued AGC, an additional 25 days (plus processing) would have been needed for a 5-acre site*
Moving Target Mortar Range – North
Initial dynamic MetalMapper 2x2 data (where thought to be usable) indicates ~1,000 sources per acre would need cued AGC
Interim one-pass AGC results showing similar sources per acre, with good reductions without need for cued AGC
APEX one-pass AGC data over same area – good agreement between data sets
MetalMapper 2x2 AGC data
APEX data. Squares are detections, Xs are required digs.
(Jacobs 2023)
Notes: *Note: 25 extra field days is based on ~200 cued shots per day, and assumes all 5ac*1,000source/ac=5,000 sources would’ve been cued (i.e., no Saturated Response Areas, no suspected culture). This is unlikely in practice. However, the additional field effort for cued data collection, then the necessary processing of cued data, would certainly have added schedule and costs to this project.

## Slide 53: One-Pass AGC: Break for questions and comments

## Slide 54: Presentation Overview
Introduction
Background on MR Technologies
SLAM Overview
One-Pass AGC Overview
Quality Requirements for MR Projects
Conclusions and Useful References

## Slide 55: Quality Requirements for MR Projects
Quality Control (QC)
“QC is a product‐oriented technique or activity designed to evaluate a completed task or product. … The quality is determined by comparing a completed product against the requirements which were developed for that product.”
Quality Assurance (QA)
“QA is a process‐oriented technique that ensures all processes are defined and appropriate. QA reviews should focus on the process elements of a project, including a review of whether project requirements are defined at the proper level of detail.”
(NAVFAC EXWC, 2019)
Quality Requirements for MR Projects
Notes: Generally,
QC: contractor’s check
QA: Government’s (or third-party designee’s) check

## Slide 56: Quality Requirements for MR Projects
AGC demands greater quality management, plus accreditation
Quality Management: Program activities involved with all aspects of quality
Quality Assurance: Audit project activities against planning documents
Quality Control: Audit project against planned or standard measurement quality objectives
Quality Control
Verify data
Validate data
Quality Assurance
Audit against planning docs
Third-party data verification/validation
Validate results
Quality Management
Personnel Requirements
Qualifications
Training
Project Planning
QAPPs
Work Plans
MQOs
System Maintenance
Hardware upgrades
Software upgrades
SOPs
MQO: Measurement Quality Objective
QAPP: Quality Assurance Project Plan
SOP: standard operating procedure
Quality Requirements for MR Projects
(Jacobs 2023)

## Slide 57: Quality Requirements for MR Projects
Ensure quality of data being collected
Ensure that collected data and derived products are sufficient to support conclusions
Document QA/QC findings so team can be assured of quality of results
Quality Requirements for MR Projects
Notes: Note: documentation is critical to QA/QC.

## Slide 58: Quality Requirements for MR Projects
Intergovernmental Data Quality Task Force
QAPP toolkits for
  RIs (April 2020)
  Remedial Actions (March 2023)
More than just requirements for sensors and similar
Quality Requirements for MR Projects
(DoD 2020, 2023)
Notes: They’re toolkits! Not templates. There is room for some healthy ribbing on contractors’ use as a template.
QAPP toolkit is STARTING POINT for a QAPP.
QAPPs are more than requirements for technologies, sensors, and similar.
Not all aspects of the toolkits’ sample project apply to every site. The toolkit sample projects are intended to be complex examples to help with planning and development of a project’s QAPP.

## Slide 59: Presentation Overview
Introduction
Background on MR Technologies
SLAM Overview
One-Pass AGC Overview
Quality Requirements for MR Projects
Conclusions and Useful References

## Slide 60: Conclusions
SLAM is available for use in GPS-denied environments, allowing use of AGC sensors and development of rich CSMs
AGC is moving toward one-pass method, but exceptions will persist
QAPPs are available (and necessary) to ensure quality outcomes for MR projects
Conclusions and Useful References

## Slide 61: Useful References
DENIX site: https://www.denix.osd.mil/mmrp/
DENIX’s AGC site: https://www.denix.osd.mil/mmrp/advanced-geophysical-classification-accreditation-and-other-tools/
Interstate Technology and Regulatory Council guidance on QA/QC of AGC: https://qcmr-1.itrcweb.org/
Navy's Basic and Advanced Munitions Response Site Management Courses: https://www.netc.navy.mil/Commands/Center-for-Seabees-and-Facilities-Engineering/Naval-Civil-Engineer-Corps-Officers-School/Courses/Environmental-Restoration/
Navy’s Guidance for Munitions Response Remedial Investigations and Feasibility Studies: Technical Report WEB‐NAVFAC‐EXWC‐EV‐1906, June 2019, Munitions Response Remedial Investigation/Feasibility Study Guidance
DENIX: DoD Environment, Safety, and Occupational Health Network and Information Exchange
Conclusions and Useful References

## Slide 62: Points of Contact
Presenter
Steve Saville
Jacobs
Steve.Saville@Jacobs.com
Topic Champions
Alexandria Hairabedian
NAVFAC EXWC
Alexandria.M.Hairabedian.civ@US.Navy.mil
Bryan Harre
NAVFAC EXWC
Bryan.L.Harre.civ@US.Navy.mil
Conclusions and Useful References

## Slide 63: Questions

## Slide 64: Backup Slides

## Slide 65: Background on MR Technologies
Background on MR Technologies
Summary of MR technologies and their objectives
  Classification – focus on the munitions
    As we covered, most subsurface metallic objects are not munitions related
    AGC, uses multi-axis EM sensors to collect a tremendous amount of data, then software to invert data to identify source(s) (that is, tangible objects) most likely to have caused the measured data
EM: electromagnetic
Notes: Inversion = mathematical process to identify the cause(s) behind measured data

## Slide 66: Background on MR Technologies
Background on MR Technologies
Summary of MR technologies and their objectives
  Classification – focus on the munitions
    As we covered, most subsurface metallic objects are not munitions related
    AGC, uses multi-axis EM sensors to collect a tremendous amount of data, then software to invert data to identify source(s) (that is, tangible objects) most likely to have caused the measured data
Notes: Inversion=mathematical process to identify the cause(s) behind measured data

## Slide 67: SLAM + AGC Case Study Results
SLAM Overview
2020 Pilot Study at Marine Corps Base Quantico
DAM: dynamic data
GDB: database
m: meter(s)
MPC: Measurement Performance Criteria (Pass/Fail)
QC: quality control
Left: Concurrent RTK + SLAM positional data
Blue dots: RTK-GPS positions Red/Green/Yellow dots: SLAM positions
Typical RTK-to-SLAM offset ~7 centimeters
Right: Distance between QC seed location (center of circle) and targeted locations (blue circles)